## Slide 1
RNS INSTITUTE OF TECHNOLOGY, BENGALURU — DEPARTMENT OF ECE
Privacy-Preserving Through-Wall Human Activity Recognition Using WiFi-CSI Without Cameras
ESP32-S3 Commodity Hardware • 5-Class Deep Learning • Multi-Seed Evaluation • Eldercare Fall Detection
PROJECT TEAM (GROUP 10) — 2026-2027
• Md Mehar Adil D H [1RN23EC094]
• Mohith Gowda M [1RN23EC095]
• Nihar Gowda [1RN23EC106]
• Sujal L G [1RN23EC169]
ACADEMIC ADVISORY
Project Guide:
Dr. Leena Chandrashekar
Associate Professor, Dept. of ECE
Project Reviewer:
Dr. Srikanth G N
Associate Professor, Dept. of ECE

## Slide 2
INTRODUCTION & CONTEXT
Motivation & Problem Statement: The Case for WiFi CSI
Speaker 1
1. Camera-Based Sensing
Major Drawbacks:
• Severe privacy invasion in private living spaces (bedrooms, restrooms).
• Strict optical Line-of-Sight (LOS) requirement.
• Completely blocked by opaque partitions, walls, and smoke.
• Fails in darkness or harsh glare.
• High storage and computational bandwidth for continuous video streams.
2. Wearable-Based Sensing
Major Drawbacks:
• Requires active user compliance and daily recharging.
• Older adults and dementia patients frequently forget or refuse devices.
• Removed during sleep or bathing (where over 60% of senior falls occur!).
• Skin irritation and discomfort with prolonged attachment.
• Costly multi-device replacements when lost or broken.
3. Proposed WiFi-CSI Sensing
Core Advantages:
• 100% Privacy-Preserving: Captures zero images or voice recordings.
• Through-Wall Capability: 2.4 GHz RF waves penetrate drywall and brick.
• Device-Free & Contactless: User wears nothing and needs zero interaction.
• Ultra Low Cost: Built with two ESP32-S3 boards (~INR 3,000 total).
• Multi-Purpose: Turns existing ambient Wi-Fi infrastructure into an active sensor.

## Slide 3
RF PHYSICAL LAYER
WiFi-CSI Fundamentals: Physical Principle & Multipath Propagation
Speaker 1
Frequency-Domain Channel Estimation in OFDM
Channel Estimation Model: Y_k = H_k · X_k + N_k ==> Ĥ_k = Y_k / X_k
Wi-Fi (802.11n) transmits over orthogonal subcarriers. The receiver estimates the complex transmission coefficient H_k = |H_k| · e^(jφ_k) from the known Long Training Field (LTF) symbols in every packet preamble.
Multipath Decomposition & Human Motion
Channel Sum: H_k(t) = H_k^s (static room) + H_k^d(t) (human)
• Static Paths (H^s): Reflections off stationary walls, floor, and furniture.
• Dynamic Path (H^d): Bounces off the moving human body.
• Constructive/Destructive Interference: Amplitude oscillates between |H^s| - |H^d| and |H^s| + |H^d|.
• Walking creates periodic cyclic swings; Falling causes an abrupt transient spike followed by a new static state.
Wavelength & Doppler Sensitivity
At 2.462 GHz: λ = c / f = 3×10^8 / 2.462×10^9 ≈ 12.2 cm
• Phase Shift: Moving the body by λ/4 ≈ 3 cm changes the reflected round-trip path by 6 cm (λ/2 = 180° phase flip).
• Sub-Centimeter Sensitivity: Even subtle breathing or sitting posture changes produce detectable phase shifts.
• Doppler Shift: f_D = 2v / λ. Walking at 1 m/s produces a ~16 Hz Doppler fluctuation, well within our 100 Hz sampling rate.
• CSI vs. RSSI: RSSI is 1 scalar average; CSI provides 90 separate frequency measurements, resolving multipath.

## Slide 4
SYSTEM IMPLEMENTATION
Experimental Hardware Architecture & Through-Wall Testbed
Speaker 1
Transmitter (TX)
Hardware: ESP32-S3 Development Board (Xtensa LX7 @ 240 MHz).
Antenna: 6 dBi omnidirectional 2.4 GHz dipole antenna.
Protocol: ESP-NOW broadcast (connectionless, 0 association latency).
Rate: 100 packet send attempts/second (T = 10 ms period).
PHY Mode: 802.11n HT40 (40 MHz bandwidth) on Channel 11 (2.462 GHz).
Fixed MAC: 1A:00:00:00:00:00 (locally administered address for receiver filtering).
Through-Wall Testbed Setup
Partition Obstruction: Dense visual partition board blocking optical LOS.
Geometry: TX on one side, person in center, RX on opposite side (~3–4 m distance).
Activities: Empty room, Sitting, Standing, Walking, Falling.
Safety Grounding: Gym crash mats for human subject safety during falling trials.
Why 40 MHz (HT40)?: Doubles bandwidth from 20 to 40 MHz, capturing 128 HT-LTF subcarriers for finer multipath resolution.
Receiver (RX) & Host PC
Hardware: ESP32-S3 board in promiscuous Wi-Fi station mode.
Directional RX: 8 dBi ALFA directional patch antenna (concentrates sensitivity toward sensing area).
CSI Extraction: ESP-IDF `esp_wifi_set_csi_rx_cb()` hardware callback.
Payload: 384 bytes (192 complex I/Q subcarrier pairs per packet).
Serial Transport: 921,600 baud USB-serial to Host PC.
Offline Processing: Python signal processing pipeline and PyTorch deep neural networks.

## Slide 5
DATA ENGINEERING
CSI Data Engineering: From Raw Bytes to Model-Ready Tensors
Speaker 2
1. Validation & Parsing
Keep valid CSI_DATA lines with exactly 25 comma-separated fields and 384 signed 8-bit integers.
Why: Rejects corrupt packets; ensures integrity.
2. Amplitude Extraction
Pair raw integers into in-phase (I) and quadrature (Q): |H_k| = sqrt(I^2 + Q^2).
Why: Amplitude is immune to random CFO/SFO oscillator phase drift.
3. Null-Carrier Drop
Drop zero amplitudes corresponding to DC subcarriers and guard bands (leaves ~108 valid carriers).
Why: Eliminates dead hardware zones.
4. Resampling to 90
Piecewise linear interpolation maps active subcarriers onto 90 standardized positions.
Why: Guarantees fixed tensor dimension across all packets.
Temporal Windowing & Model Input Shape: [Batch, 1, 250, 90]
Window Length W = 250 packets (~2.5 seconds @ 100 Hz) | Stride S = 50 packets (0.5 second advance, 80% overlap)
• 2.5 seconds of context captures complete sit-to-stand transitions, several walking strides, or a complete fall-and-rest sequence. • Overlap multiplies training samples and prevents critical events from being severed at window boundaries. • Final model-ready tensor per sample: 250 time packets × 90 amplitude features.

## Slide 6
REPRODUCIBILITY AUDIT
Critical Scientific Audit: Discovering Window-Level Data Leakage
Speaker 2
The Overlap Leakage Diagnosis
Critical Audit Finding:
• The legacy dataset had 2,241 windows created with stride 50 (80% overlap = 200 packets shared between adjacent windows).
• The 70/15/15 train/val/test split was performed AT THE WINDOW LEVEL.
• Consequently, Window i in Train shared 80% of identical raw packets with Window i+1 in Test!
• Over 90% of test windows had near-identical sister windows in the training set.
• The model easily achieved 97%–98% test accuracy by interpolating adjacent frames and memorizing the room's static multipath fingerprint.
Empirical Proof: Generalization Collapse
Testing 97.63% Checkpoint on 25 Unseen Recordings:
• We collected 25 new unseen recording sessions in `live_recordings/`.
• When evaluated on these unseen recordings, accuracy collapsed from 97.63% to 20.55% (no better than random guessing across 5 classes!).
• Recording-level majority vote accuracy: only 20.00% (5 of 25 correct).
• Why? Receiver Automatic Gain Control (AGC) shifted amplitude ranges (max jumped from 25.88 to 277.19), saturating uncalibrated inputs.
• Conclusion: Prior 98% accuracy claims measured memorization, not true generalized through-wall sensing.

## Slide 7
DATA ENGINEERING
Dataset Enrichment & The Leakage-Resistant Grouped Protocol
Speaker 2
Dataset Expansion: 51 Original Recordings + 25 New Recordings = 76 Sessions
Class | Original Files | Original Windows | New Files | New Windows | Total Files | Total Windows | Class Share Empty | 20 | 841 | 5 | 118 | 25 | 959 | 34.4% Sitting | 10 | 471 | 5 | 108 | 15 | 579 | 20.7% Standing | 9 | 409 | 5 | 92 | 14 | 501 | 18.0% Walking | 11 | 477 | 5 | 125 | 16 | 602 | 21.6% Falling (!) | 1 | 43 | 5 | 107 | 6 | 150 | 5.4% Total | 51 | 2,241 | 25 | 550 | 76 | 2,791 | 100.0%
The Recording-Grouped Protocol
• Recording-Level Quarantine: Entire CSV files are assigned to Train, Val, or Test BEFORE windowing. • Strictly Zero Overlap: 0% packet sharing between train and test sets. • Train: 53 files (1,945 windows) | Val: 11 files (369 windows) | Test: 12 files (477 windows).
Train-Only Normalization & Class Weights
• Scaling statistics (min, max, μ, σ) are computed EXCLUSIVELY on training recordings and frozen for test and live inference. • Falling Class Weighting: w_c = N / (C · N_c) assigns a 3.78× loss penalty to missed falls, preventing the model from ignoring the minority class.

## Slide 8
DEEP LEARNING ARCHITECTURES
Model Evolution: Grounding Neural Networks in RF Physics
Speaker 3
1. The Crucial Input Layout Correction
The Wrong Layout [B, 250, 90]:
• PyTorch Conv1D treats dimension 1 as channels. • [B, 250, 90] treated 250 time packets as unordered channels and slid filters across the 90 subcarriers. • Temporal order was destroyed in the first layer! Accuracy capped at 91.10%.
The Correct Layout [B, 90, 250]:
• Permute tensor to [B, 90, 250]. • 90 CSI subcarriers are channels; Conv1D slides along 250 time steps. • Acts as a learned temporal filter bank detecting Doppler oscillations across frequency. • Single change increased accuracy from 91.10% to 97.63%!
2. Original Baseline: CNN-BiLSTM (319k Params)
Layer-by-Layer Architecture:
• Input: [B, 1, 250, 90] -> squeeze + permute -> [B, 90, 250]
• Conv1D 1: 90 -> 64 channels (kernel 5, padding 2) + BN + ReLU (28,864 params)
• Conv1D 2: 64 -> 128 channels (kernel 3, padding 1) + BN + ReLU (24,704 params)
• MaxPool1D: kernel 2, stride 2 (halves time: 250 -> 125 steps)
• BiLSTM: input 128, hidden 128, 1 layer (2 directions: 264,192 params)
• Concat States: ht[-2] (forward) + ht[-1] (backward) = 256 features
• Classifier: Dropout(0.1) + Linear(256 -> 5) (1,285 params)
• Total Parameters: 319,429 | Historical Acc: 96.54% ± 2.03%

## Slide 9
ARCHITECTURAL INNOVATION
Proposed Novel Architectures: MS-CNN-BiGRU & SE-TCN
Speaker 3
Proposed 1: MS-CNN-BiGRU (188k Params)
Multi-Scale Temporal Filter Bank:
• Multi-Scale Convolutions: Parallel branches with kernels k=3 (30 ms fall spikes), k=5 (walking cadence), and k=7 (slow posture shifts).
• Subcarrier SE Attention: Squeeze-and-Excitation dynamically suppresses low-SNR fading notch subcarriers.
• Bidirectional GRU (hidden 96): Eliminates separate cell state, saving 33% recurrent parameters.
• Parameter Reduction: 188,673 params (41% smaller than 319k baseline).
• Legacy Test Accuracy: 97.09% ± 0.95% (cuts baseline variance in half!).
Proposed 2: SE-TCN Champion (110k Params)
Non-Recurrent Dilated Temporal Network:
• Fully Convolutional: No recurrent bottlenecks; fully parallelized on CPU with 2.75 ms latency.
• Exponential Dilations (d = 1, 2, 4, 8): Receptive field spans the entire 2.5s window without vanishing gradients.
• Global Average Pooling: Eliminates dense linear parameters and prevents temporal boundary overfitting.
• Extreme Efficiency: Only 110,165 parameters (65.5% smaller than baseline).
• Unseen Session Accuracy: 58.57% ± 2.64% (+9.18% higher than CNN-BiLSTM on true generalization!).

## Slide 10
EMPIRICAL EVALUATION
Experimental Results: Controlled Multi-Seed Benchmarks
Speaker 4
Multi-Seed Benchmark: Legacy Split vs. Leakage-Free Grouped Split
Model | Parameters | Latency | Legacy Random Split Acc | Grouped Leakage-Free Acc | Grouped Bal. Acc | Grouped Fall Recall MLP | 11,588,101 | 1.37 ms | 89.91% | 46.33% | 39.67% | 26.32% LeNet (2D CNN) | 163,813 | 4.00 ms | 96.44% | 52.41% | 42.23% | 0.00% (Blind to falls) BiLSTM | 80,517 | 1.56 ms | 72.11% | 41.93% | 48.67% | 94.74% (Severe false alarms) CNN_GRU | 153,669 | 2.76 ms | 97.63% | 45.28% | 35.39% | 0.00% (Blind to falls) CNN_BiLSTM (Base) | 319,429 | 2.39 ms | 94.36% ± 2.16% | 49.39% ± 3.89% | 46.26% | 45.26% MS_CNN_BiGRU (Ours) | 188,673 | 12.8 ms | 97.09% ± 0.95% | 50.02% ± 4.63% | 45.28% | 29.47% SE_TCN (Champion) | 110,165 | 2.75 ms | 97.15% ± 0.61% | 58.57% ± 2.64% (Best 62%)| 55.46% | 47.37%
Ablation A: Loss Function for Fall Sensitivity
• Standard Cross-Entropy: Fall Recall = 10.53% (missed 17 of 19 falls!). • Class-Weighted CE: Fall Recall = 15.79% (Macro-F1 improves to 0.4874). • Focal Loss (γ = 2.0): Fall Recall = 31.58% (3× higher fall sensitivity!).
Ablation B: Normalization Scheme Stability
• Train Min-Max: 58.07% accuracy across unseen recordings. • Z-Score Standardization ((x - μ)/σ): 58.49% accuracy (best gain stability). • Dynamic Demean (x - x_mean): 49.27% (confirms static baseline carries sitting/standing height profile).

## Slide 11
LITERATURE CONTEXT
Literature Comparison: Strohmayer & Kampel (2023) vs. Our System
Speaker 4
Base Paper: Strohmayer & Kampel (ICVS 2023)
Hardware: 2× ESP32 with hand-built copper biquad antennas.
Radio: ESP-NOW broadcast @ 100 Hz, 20 MHz bandwidth (52 L-LTF subcarriers).
Environment: 18 m hallway through 4 structural brick walls.
Task: 3 coarse classes: Empty, Walking, Walk+Wave.
Model: EfficientNetV2-S (2D Image CNN with ~20 Million parameters).
Reported Result: 97.43% ± 1.1% (LOS) / 88.16% ± 4.6% (Through 4 walls).
Key Limitation: Heavy 20M parameter model; only 3 coarse dynamic movements; no fall detection.
Our Work: ESP32-S3 + SE-TCN / MS-CNN-BiGRU
Hardware: 2× ESP32-S3 boards with 6 dBi omni TX and 8 dBi patch RX.
Radio: ESP-NOW broadcast @ 100 Hz, 40 MHz HT40 (192 subcarrier entries -> 90 features).
Environment: Short range through opaque visual partition board.
Task: 5 fine-grained classes: Empty, Sitting, Standing, Walking, Falling.
Model: SE-TCN (110k params) & MS-CNN-BiGRU (188k params) — 180× more compact!
Results: 97.15% ± 0.61% (Legacy split) / 58.57% ± 2.64% (Unseen sessions).
Defense Point: We do not claim our model outperforms Strohmayer; our setup evaluates a harder 5-class problem at 180× smaller model size.

## Slide 12
DEPLOYMENT & VIVA DEFENSE
Live Inference Pipeline, Practical Limitations & Future Roadmap
Speaker 4
Live Streaming Inference Engine
Operational Architecture:
• FIFO Buffer: Maintains rolling queue of the latest 250 packets (~2.5s).
• Pipeline Consistency: Applies exact amplitude extraction, null-drop, interpolation to 90 features, and training-fitted normalization.
• Inference Cadence: Evaluates every 50 packets (0.5s stride) with 2.75 ms compute latency.
• Prediction Smoothing: 3-window majority vote prevents visual flickering.
• Eldercare Fall Alert: Triggers emergency dispatch alert when P(Falling) >= 0.50 followed by prolonged stillness.
Honest Limitations & Project Conclusion
Limitations & Future Roadmap:
• Cross-Environment Domain Shift: Tested in single room; moving furniture changes static multipath (addressed via few-shot fine-tuning).
• Multi-Person Interference: Superimposed reflections require multi-antenna Angle-of-Arrival (AoA) decomposition.
• Phase Sanitization: Adding sanitized phase differences between packets is listed as future work.
• Microcontroller Quantization: At 110k parameters, SE_TCN is ready for INT8 quantization on the ESP32-S3's 8 MB PSRAM.
• Conclusion: Validated that commodity ESP32-S3 Wi-Fi provides a robust, privacy-preserving, camera-free sensing modality.

## Slide 13
THANK YOU!
Privacy-Preserving Through-Wall Human Activity Recognition Using WiFi-CSI
Group 10 • Dept. of ECE, RNS Institute of Technology • 2026-2027 Questions & Panel Discussion